## Slide 1: Noise (Electrical)
PHY2250 Electronics & Circuit Theory

## Slide 2: “Noise”
Definition: For our purposes, “noise” is any ‘unwanted’ contribution to a “signal”
Unlike other discussions of noise, we do not require ‘noise’ to be random.
  Rather, it could simply be an additional audio waveform which interferes with our intended signal
  “Hum” also counts as “noise” for this discussion

## Slide 3: Noise Sources
Main sources:
  Poor ground - “60 Cycle Hum”
  ‘Other’ circuits turning off & on
  Induced via electromagnetic fields

## Slide 4: Signal-to-Noise Ratio (SNR)
“the ratio of the strength of an electrical or other signal carrying information to that of interference, generally expressed in decibels.”
      Wikipedia
SNR (dB) = 10 log10 (PowerSignal / PowerNoise )
= 10 log10 (VSignal2 / VNoise2 )
= 20 log10 (VSignal / VNoise )

## Slide 5: Noise Countermeasures
“Good ground”
Common Mode Rejection
“Choke”: Low-Pass Filter.
Smart cable practices

## Slide 6: Good Ground
Signal is typically a voltage, which is a potential difference
  If noise is on both “signal” and “ground”, it subtracts out!
  Recall improvements via using ground clip on scope
Multiple components should be on same circuit (e.g., “amp fighting” in Taylor video)
Can also Isolate (“ground lift”) via transformer

## Slide 7: Common Mode Rejection
Featured in
  Differential amplifier
  Balanced connection: Same signal on two wires, but one is inverted; then invert again & sum
  Course notes:

## Slide 8: Choke
A choke is a Low-Pass Filter (LPF)
Since noise is typically high-frequency, running a LPF can often help significantly improve SNR
A choke is typically a single inductor placed in series with the signal
Fancier chokes may use one or more inductors in series with main signal flow, possibly combined with capacitor in parallel:
More on chokes, from guitar amp manufacturer:
http://www.aikenamps.com/index.php/chokes-explained

## Slide 9: Smart Cable Practices
Alternate (/Reverse) the Winding Direction of Coils
  Used to reduce E/M interference
  Examples:
    “Over/under” cable wrap – also puts lets stress on wires in cable, plus allows for easy uncoiling.
    Humbucker guitar pickups
Don’t mix power & ‘data’/’signal’ cables
  i.e., don’t have them near each other
Cross at right angles rather than run parallel